Question 1.

θ1 = 15o / θ2 = 5o / θ3 = 25o	c1 = 1.25 m / c2 = 0.75 m	M∞ = 25 / α = 10o	halt = 35 km / T∞ = 237 K / p∞ = 559 pa

Calculate (β-δ), the static pressure (P1), static temperature (T1), and static density (ρ1) on the upper surface (1) using the calorically perfect gas (CPG) assumption and the thermo-chemical equilibrium assumption to solve.

The values for flow deflection will be constants dependent on the geometry.

Face 1:
%delta_1 = %theta_1 - %alpha
Face 2:
%delta_2 = %theta_2 + %alpha
Face 3:
%delta_3 = %theta_3 - %theta_2
a) CPG assumption

tan %delta = 2 cot %beta left [ { { M^2 sin^2%beta - 1 } over { M^2 (%gamma + cos 2 %beta) + 2 } } right ]	(1)

This can be solved numerically using the Newton or Secant root finding method or by using a on-line calculator or table. For this solution an implementation of the secant method was used.

Secant Method:
For function (where n is the face number and the free stream is relative to the face n)
f(%beta^n) = 2 cot %beta^n left [ { { M_infinity^2 sin^2%beta^n - 1 } over { M_infinity^2 (%gamma + cos 2 %beta^n) + 2 } } right ] - tan %delta^n	(2)
where δ is known.

Apply the algorithm:

select initial guesses of β1 and β0 / while tolerance not met loop / %beta_{i+1} = %beta_i - {f(%beta_i) (%beta_i - %beta_{i-1})} over {f( %beta_i ) - f(%beta_{i-1})} / check tolerance against |βi+1 - βi| / update shock angle values for next iteration as βi to equal βi+1 and βi-1 to equal βi / end loop and return βi+1

From the resulting shock angle β, CPG relations can be used for pressure, density, and temperature ratios to obtain the static flow properties over the surface. **Note these subscripts do not correspond to the surfaces in the figure for this problem.**
{p_2} over {p_1} = 1 + { 2 %gamma } over { %gamma +1 } ( M_1^2 sin^2 %beta - 1 )	(3)

{T_2} over {T_1} = { p_2/p_1 } over { %rho_2/%rho_1 } = { left [1 + { 2 %gamma } over { %gamma +1 } ( M_1^2 sin^2 %beta - 1 ) right ] left [{ (%gamma -1)M_1^2sin^2%beta + 2 } right ] } over { { (%gamma +1)M_1^2sin^2%beta } }	(4)

{%rho_2} over {%rho_1} = { (%gamma +1)M_1^2sin^2%beta } over{ (%gamma -1)M_1^2sin^2%beta + 2 }	(5)

CPG assumption results:
Face↓	(β-δ)	P [Pa]	T [K]	ρ [kg/m3]
1	0.031187	5,599.3	622.31	0.031362
2	0.059923	40,660	3,103.0	0.045673
3	0.133536	433,750	8487.4	0.17813

b) Thermo-chemical equilibrium assumption

This approach requires an iterative procedure as follows:

Select initial guess for ε1 and ε0, usually 0.1 and 0.001 respectively / Loop while abs {f(%epsilon)} > tolerance / (1) %epsilon = %rho_1/%rho_2 / (2) tan %beta = { (1-%epsilon)-sqrt{(1-%epsilon)^2 - 4%epsilon tan^2 %delta} } over { 2 %epsilon tan %delta } / (3) u_{ 1n } = u_1 sin %beta / (4) u_{ 2n } = %epsilon u_{ 1n } / (5) p_2 = p_1 + %rho_1 u_{ 1n }[ 1-%epsilon ] / (6) h_2 = h_1 + u_{ 1n }^2 over 2[ 1-%epsilon^2 ] / (7) tilde h_2 = tilde h_2 ( %rho_2, p_2 ) / (8) f(%epsilon) = h_2(%epsilon) - tilde h_2(%epsilon) / (9) Apply secant method to step (8) to obtain next value for εi+1 / %epsilon_{i+1} = %epsilon_i - {f(%epsilon_i) (%epsilon_i - %epsilon_{i-1})} over {f( %epsilon_i ) - f(%epsilon_{i-1})}

The values for static pressure, and density fall out of this method directly. To obtain the static temperature the relation T = T(ρ,p) is used.

Thermo-chemical equilibrium assumption results:

Face↓	(β-δ)	P [Pa]	T [K]	ρ [kg/m3]
1	0.030751	5,580.8	605.27	0.031689
2	0.047308	39,113	2,437.9	0.055454
3	0.070615	458,340	4,067.1	0.34981

c) Comparison of results obtained in parts (a) and (b).

Percent Difference Results:

Face↓	(β-δ) [%]	P [%]	T [%]	ρ [%]
1	1.41813	0.33217	2.81376	1.03142
2	26.66596	3.95533	27.28175	17.63855
3	89.10380	5.36565	108.68590	49.07832

From these results it can be seen that the pressure is the least effect by the CPG assumption vs the equilibrium assumption. The temperature was most effected by the CPG assumption. Both of these results make sense based on the assumptions made for each method. For equilibrium the vibrational mode is being considered. Energy that would have been seen in the translational mode (measured by temperature) is now being used in the vibration of the molecules. Pressure however is only dependent of the number of collisions on the surface, which is not effected by energy but rather momentum. Finally a correlation can be drawn between the errors seen by the shock layer thickness (β-δ) and the density. In hypersonic flow the shock layer will be smaller using the Equilibrium approach as opposed to using the CPG approach. With a smaller shock layer there smaller volume between the surface and the shock boundary. As a result, there will be more compression of the mass behind the shock, causing a higher density.

d) Calculate the compressibility factor (z) and the molecular weight (M) of the mixtures on each face.

For air R0 = 286.9 [J/kg K] and M0 = 28.97 [kg/kg-mol]

In class the following relations relation was derived.
z = M_0 over M = R over R_0	(6)

From this it state equation can be written in terms of the reference gas constant at STP, and the static state variables on a face, and the compressibility. From this the compressibility can be solved for in terms of known variables.
p = %rho R_0 left( R over R_0 right ) T = %rho R_0 z T => z = p over { %rho R_0 T }	(7)

Finally once compressibility of the mixture is known, the molar mass (M) of the mixture can be found from the reference molar mass of air at STP and the compressibility.
M = M_0 over z	(8)

Results: **using the equilibrium results from part (b)
Face↓	z	M [kg/kg-mol]
1	1.0142	29.551
2	1.0084	29.720
3	1.1229	26.689

e) Calculate the pressure coefficient on each face using the results from CPG, thermo-chemical equilibrium, and the hypersonic similarity parameter (HSP).

For both CPG and equilibrium, the results obtained in parts (a) and (b) can be used to calculate the pressure coefficients. The HSP will require an additional calculation as will be shown shortly.
c_p = { p - p_infinity } over { q_infinity } = 2 over { %gamma M_infinity^2} left ( p over p_infinity -1right )	(9)

Equation 9 applies to all cases not only to CPG even though a constant specific heat ratio (γ). This can be shown, but is just accepted here.

For the HSP the relations in equations 10 and 11 are used to obtain the pressure ratio.
%KAPPA = M_{up-stream} %delta	(10)

p_{down-stream} over p_{up-stream} = 1 + { %gamma(%gamma +1) } over 4 %KAPPA^2 + %gamma%KAPPA^2 sqrt { left ( {%gamma +1} over 4 right)^2+ 1 over {%KAPPA}^2 }	(11)

Notice that the pressure ratio is not with the free-stream pressure but the pressure upstream of the shock. As a result face 3 will need to be corrected to give a pressure coefficient value that is with respect to the free-stream. The procedure to do this is as follows.

1. Calculate the pressure coefficient on face 3 with respect to the conditions seen on face 2. ie.
p_{3} over p_{2} = 1 + { %gamma(%gamma +1) } over 4 %KAPPA^2 + %gamma%KAPPA^2 sqrt { left ( {%gamma +1} over 4 right)^2+ 1 over {%KAPPA}^2 }	(12)

were %KAPPA = M_2 %theta **Note: The Mach number on face two was found using the CPG assumption. This is acceptable because the HSP is derived using this assumption in addition to other assumptions.

2. Using equation 9, the pressure on face 3 and the pressure on face 2 were backed out. **The Mach number is still from the CPG assumption for face 3.

3. Finally the pressure coefficient on face three was re calculated using the pressure found on face 3 using the HSP assumptions and the free-stream conditions.

Results:
Face↓	Equilibrium	CPG	HSP
1	0.020534	0.020610	0.020639
2	0.157646	0.163972	0.167118
3	1.871829	1.771270	1.808017

f) Find L/D using each method from part (e)

Derivation of cl and cd in terms of free-stream conditions and pressure coefficients on each face.

X and Y-direction forces, A and N respectively.
N = -p_1 A_1 cos %theta_1 + p_2 A_2 cos %theta_2 + p_3 A_3 cos %theta_3

A = p_1 A_1 sin %theta_1 + p_2 A_2 sin %theta_2 + p_3 A_3 sin %theta_3 - p_infinity A_4

From the geometry, the areas can be expressed as:
A_1 = { c_1 + c_2 } over { cos %theta_1 } A_2 = { c_1 } over { cos %theta_2 } A_3 = { c_2 } over { cos %theta_3 } A_4 = (c_1 + c_2)tan %theta_1 + c_1 tan %theta_2 + c_2 tan %theta_3

With some algebra, N and A can be re-written as: (S = c1 + c2)
N = -(p_1 - p_infinity) S + (p_2 - p_infinity) c_1 + (p_3 - p_infinity) c_2

A = (p_1 - p_infinity) S tan %theta_1 + (p_2 - p_infinity) c_1 tan %theta_2 + (p_3 - p_infinity) c_2 tan %theta_3

These equations can now be used in the lift and drag equations:
L = N cos %alpha - A sin %alpha D = N sin %alpha + A cos %alpha

And then into the lift and drag coefficient equations:
c_L = L over { q_infinity S } c_D = D over { q_infinity S }

With some more algebra it can be shown then that:

c_L = (-c_{p1} + c_{p2} c_1 over S + c_{p3} c_2 over S ) cos %alpha - (c_{p1}tan %theta_1 + c_{p2} {c_1 tan %theta_2} over S + c_{p1} {c_2 tan %theta_3} over S) sin %alpha

c_D = (-c_{p1} + c_{p2} c_1 over S + c_{p3} c_2 over S ) sin %alpha + (c_{p1}tan %theta_1 + c_{p2} {c_1 tan %theta_2} over S + c_{p1} {c_2 tan %theta_3} over S) cos %alpha

From these values the L/D term can be found as:
L over D = c_L over c_D

Results:

	Equilibrium	CPG	% error	HSP	%error
cl	0.70879	0.6784	4.2788	0.69280	2.2569
cd	0.47169	0.44886	4.8403	0.45809	2.8826
L/D	1.5027	1.5115	0.59010	1.5124	0.64432

The best method used here is the equilibrium method.
Question 2.

a) Derive an expression for the Gas constant of the given mixture in terms of moles of each species. Y1 is the number of moles of N2 and Y2 is the number of moles of He.

Staring with:
tilde R = sum from i = 1 to N c_i R_i = c_{ N_2 } R_{ N_2 } + c_{ He } R_{ He }

using the relation:
c_i = { %rho_i } over { tilde %rho } = N_i over N where N = Y_1 + Y_2

Rearrange:
tilde R = Y_1 over {Y_1 + Y_2} R_{ N_2 } + Y_2 over {Y_1 + Y_2} R_{ He }

Substitute the values and pull out the universal gas constant:
tilde R = 8314.32 over {Y_1 + Y_2} left [ Y_1 over 28.0 + Y_2 over 4.002602right ]
b) Derive expressions for sensible internal energy (e) and enthalpy (h) per unit mass of mixture in terms of Y1 and Y2.

For a diatomic molecule (N2):
e = e_{ trans. } + e_{ rot. } + e_{ vib. } + e_{ el. }

For an atom (He):
e = e_{ trans. } + e_{ el. }

Neglecting the electronic excitation these simplify to:

For a diatomic gas (N2):
e = e_{ trans. } + e_{ rot. } + e_{ vib. }

For an monoatomic gas (He):
e = e_{ trans. }

Each term in these equations can then further be defined as follows:

e_{ trans. } = 3 over 2 R T e_{ rot. } = R T e_{ vib. } = { %theta_v/T } over { e^{ %theta_v/T } - 1 } R T

Substituting these terms back into the equations above results in:

For a diatomic gas (N2):
e = 5 over 2 R T + { %theta_v/T } over { e^{ %theta_v/T } - 1 } R T

For an monoatomic gas (He):
e = 3 over 2 R T

For the enthalpy per unit mass:
h = e + R T

For a diatomic gas (N2):
h = 7 over 2 R T + { %theta_v/T } over { e^{ %theta_v/T } - 1 } R T

For an monoatomic gas (He):
h = 5 over 2 R T

To find the sensible internal energy and enthalpy per unit mass for a mixture, the following equations are used:
e_s = sum from i=1 to N c_i (e_s)_i h_s = sum from i=1 to N c_i (h_s)_i
Expanding these and making the appropriate substitutions results in:
e_s = c_1 ( e_s )_1 + c_2 ( e_s )_2 = Y_1 over { Y_1 + Y_2 } ( 5 over 2 R_{N_2} + {%theta_v}_{N_2} over { e^{ {%theta_v}_{N_2}/T } - 1 } R_{N_2} T ) + Y_2 over { Y_1 + Y_2 } ( 3 over 2 R_{He} T )

e_s = {8314.32 T} over { Y_1 + Y_2 } left [ Y_1 over 28.0 left ( 5 over 2 + {3390/T} over{ e^{ 3390/T } - 1 } right ) + Y_2 over 4.002602 left ( 3 over 2 right ) right ]

h_s = c_1 ( h_s )_1 + c_2 ( h_s )_2 = Y_1 over { Y_1 + Y_2 } (7 over 2 R_{N_2} + {%theta_v}_{N_2} over { e^{ {%theta_v}_{N_2}/T } - 1 } R_{N_2} T ) + Y_2 over { Y_1 + Y_2 } ( 5 over 2 R_{He} T )

h_s = {8314.32 T} over { Y_1 + Y_2 } left [ Y_1 over 28.0 left ( 7 over 2 + {3390/T} over{ e^{ 3390/T } - 1 } right ) + Y_2 over 4.002602 left ( 5 over 2 right ) right ]
c) Iterative procedure to solve for conditions behind a normal shock, no reactions, vibrational excitation is present.

Input u1 and T1 / Select initial guess for ε1 and ε0, usually 0.1 and 0.001 respectively / Loop while abs {f(%epsilon)} > tolerance / (1) let %epsilon = %rho_1/%rho_2 / (2) u_{ 2 } = %epsilon u_{ 1 } / (3) tilde R = 8314.32 over {Y_1 + Y_2} left [ Y_1 over 28.0 + Y_2 over 4.002602right ] / (4) T_2 = %epsilon left[ T_1 +u_{ 1 }^2 over tilde R( 1-%epsilon ) right ] / (5) h_1 = h_1 (T_1) = {8314.32 T_1} over { Y_1 + Y_2 } left [ Y_1 over 28.0 left ( 7 over 2 + {3390/T_1} over{ e^{ 3390/T_1 } - 1 } right ) + Y_2 over 4.002602 left ( 5 over 2 right ) right ] / (6) h_2 = h_1 + u_{ 1 }^2 over 2[ 1-%epsilon^2 ] / (7) tilde h_2 =tilde h_2 (T_2) = {8314.32 T_2} over { Y_1 + Y_2 } left [ Y_1 over 28.0 left ( 7 over 2 + {3390/T_2} over{ e^{ 3390/T_2 } - 1 } right ) + Y_2 over 4.002602 left ( 5 over 2 right ) right ] / (8) f(%epsilon) = h_2(%epsilon) - tilde h_2(%epsilon) / (9) Apply secant method to step (8) to obtain next value for εi+1 / %epsilon_{i+1} = %epsilon_i - {f(%epsilon_i) (%epsilon_i - %epsilon_{i-1})} over {f( %epsilon_i ) - f(%epsilon_{i-1})} / end loop / %rho_2 over %rho_1 = 1over%epsilon / T_2 over T_1 = T_2 over T_1 / p_2 = %rho_2 tilde R T_2 / p_2 over p_1 = p_2 over p_1

d) Would there be a simpler approach to solve for a mono-atomic gas through a normal shock?

Yes there would be a simpler solution than using the iterative procedure. Because it is a mono-atomic gas, the CPG assumption (constant specific heat ratio) can be made so long as there is no electronic excitation of the molecules.

The specific heat ratio for a mono-atomic gas will be 1.66. As a result the following relations can be used for the normal shock relations:

{p_2} over {p_1} = 1 + { 2 %gamma } over { %gamma +1 } ( M_1^2 - 1 )

{T_2} over {T_1} = { p_2/p_1 } over { %rho_2/%rho_1 } = { left [1 + { 2 %gamma } over { %gamma +1 } ( M_1^2 - 1 ) right ] left [{ (%gamma -1)M_1^2 + 2 } right ] } over { { (%gamma +1)M_1^2 } }

{%rho_2} over {%rho_1} = { (%gamma +1)M_1^2 } over{ (%gamma -1)M_1^2 + 2 }
Question 3.

1
2
3
4
5
θ1 = 15o / θ2 = 25o	C1 = 2.0 m / c2 = 1.0 m	α = 5o

Calculate (β-δ), the static pressure (P1), static temperature (T1), and static density (ρ1) on the upper surface (1) using the calorically perfect gas (CPG) assumption and the thermo-chemical equilibrium assumption to solve.

The values for flow deflection will be constants dependent on the geometry.

Face 1:
%delta_1 = %theta_1 - %alpha
Face 2 and 4:
%delta_{2,4} = %theta_2 - %theta_1
Face 3:
%delta_3 = %theta_1 + %alpha

Newtonian theory:
c_p = 2 sin^2 %delta

Note that cp2 = cp4 because the deflection angle is the same on face 2 and 4.

Approaching this problem similarly to problem 1, the following equations were found.

X and Y-direction forces, A and N respectively.
N = -p_1 A_1 cos %theta_1 - p_2 A_2 cos %theta_2 + p_3 A_3 cos %theta_1 + p_4 A_4 cos %theta_2

A = p_1 A_1 sin %theta_1 + p_2 A_2 sin %theta_2 + p_3 A_3 sin %theta_1 + p_4 A_4 sin %theta_2 - p_infinity A_5

From the geometry, the areas can be expressed as:
A_1 = A_3 = { c_1 } over { cos %theta_1 } A_2 = A_4 = { c_2 } over { cos %theta_2 } A_4 = 2(c_1tan %theta_1 + c_2 tan %theta_2)

With some algebra, N and A can be re-written as: (S = c1 + c2)
N = -(p_1 - p_infinity) c_1 -(p_2 - p_infinity) c_2 + (p_3 - p_infinity) c_1 + (p_4 - p_infinity) c_2

A = (p_1 - p_infinity) c_1 tan %theta_1 +(p_2 - p_infinity) c_2tan %theta_2 + (p_3 - p_infinity) c_1 tan %theta_1 + (p_4 - p_infinity) c_2 tan %theta_2

These equations can now be used in the lift and drag equations:
c_l = c_N cos %alpha - c_A sin %alpha c_d = c_N sin %alpha + c_A cos %alpha

where c_L = L over { q_infinity S } c_N = N over { q_infinity S }

With some algebra it can be shown then that:

c_N = { 2 c_1 } over S [ sin^2 %delta_1 + sin^2 %delta_3 ]

c_A = { 2 c_1 tan %theta_1 } over S [ sin^2 %delta_1 + sin^2 %delta_3 ] + { 4 c_2 tan %theta_2 } over S sin^2 %delta_{ 2,4 }

From these values the L/D term can be found as:
L over D = c_L over c_D

L/D for this geometry was found to be: 2.3681